## Slide 1
NETWORKING WORLD
COMPANY HAS TWO BRANCHES

## Slide 2
ABOUT US
This project presents a network design for a company that has two branches located in different cities. The main goal is to ensure secure and efficient communication between both sites using modern networking technologies. The design includes suitable network devices, a clear topology, and proper security measures to support daily business operations, data sharing, and centralized services.

## Slide 3
COMPANY BRANCHES OVERVIEW:-
  Both branches require internet access, internal communication, and shared services such as file sharing and printing.

## Slide 4
NETWORK TOPOLOGY:-
This diagram shows two branches connected through routers using OSPF.
Each branch has VLANs, multilayer switches for routing, and access switches for connecting PCs.
Trunk links and EtherChannel are used for redundancy and faster communication.

## Slide 5
VLAN CONFIGURATION:-
VLANs are used to separate different departments within each branch for better security and traffic management.
Each VLAN has its own IP range to control network communication.
Branch A:
VLAN 10 → IP Range: 192.168.10.0/24
VLAN 20 → IP Range: 192.168.20.0/24
Branch B:
VLAN 2 → IP Range: 172.16.2.0/24
VLAN 3 → IP Range: 172.16.3.0/24

## Slide 6
ROUTING AND INTER-BRANCH
COMMUNICATION:-
.
  Branches are connected through routers using OSPF (Open Shortest Path First) inside AREA 0.
  Each router is configured to advertise its VLAN subnets.
  Secure communication between Branch A and Branch B is established over VPN tunnels.
  Dynamic routing ensures high availability and fast recovery in case of link failure.

## Slide 7
ESSENTIAL NETWORKING CONCEPTS AND SECURITY:-
Directs traffic between networks
Trunk
Connects internal devices
Switch
VLAN
Separates the network into groups to
improve security and reduce traffic.
BPDU Guard
STP
HSRP
Protects the network from rogue switches
Prevents loops that can crash the network
Provides a backup gateway if the main router fails
Router
carries multiple VLANs over one link.
DHCP
EtherChannel
PortFast
Port Security
OSPF
Automatically gives IP addresses to devices.
Combines multiple cables into one faster, more reliable link
Makes ports active faster for end devices
Limits which devices can connect to a port
Finds the best path for data quickly in big networks

## Slide 8
Ahmed Magdy Mustafa
Ahmed Samir Darwish
Ahmed Ashraf
Abdel Aziz
Saif Aleslam mohamed
Essam Elsayed Mahmoud
Amer Mohamed Abdelhamed
OUR AMAZING
TEAM:-